## Slide 1: SHADOZ (Southern Hemisphere Additional Ozonesondes) Status
Anne Thompson, anne.m.thompson@nasa.gov
May 2014, Ozone Research Managers Mtg, Geneva
Archiver: J Witte, SSAI@GSFC; http://croc.gsfc.nasa.gov/shadoz
Notes: <number>

## Slide 2: Outline of Presentation
What, Why, Where, Who of SHADOZ
Compelling New Science: “UT/LS,” Air Quality
Metrics, Impact, Archive Updates
  Reactivation of Stations
  Data Re-processing by WMO/NDACC Sonde Guidelines. Focus on 3 variables (Sensing Solution Type [SST], Instrument type, Pump Correction Factor [PCF]).
Radiosonde Variations & Impact on SHADOZ
  Background Current. Implication for SHADOZ at certain sites
  New Radiosondes (RS80-> RS92->Imet). “Pressure Offsets” - new ‘paper in AMT (Stauffer et al, 2014)
  Third (new) instrument type. SPC stable, ENSCI-> DMT ??
Summary – SHADOZ at Year 16.
  Essential to detect UT/LS ozone-climate change; pollution!
  Instrument changes will require periodic re-processing
  Management Need: Program to avoid gaps

## Slide 3
Integrated Earth Observing for Ozone
        Measure
Measure
Model
Predict
Satellites with ground-based (eg Dobson) instruments for total column
Profile validation - partial columns (lidar, aircraft); only sondes
measure surface to 5-10 hPa (35 km) with 50-100 m vertical resolution
Notes: <number>

## Slide 4: Why & How: SHADOZ Initiative: Validate 1-2 Generations of Ozone Satellites
“Strategic” ozonesonde network coordinates launches in space & time for specific scientific purposes
What is role of dynamics in ozone variability? Need 2-5 launches/month
PRACTICAL CONSTRAINTS
  Operational – host supplies ground stations, launch gas, personnel
  NASA/NOAA supply *some* sondes – ALL data open @ GSFC
  Leveraging resources key to sustaining network

## Slide 5: Where, When, Who: SHADOZ Stations & Data Archive
WHERE & WHEN are the data?
  13 stations operational. 15 in 2005-2009 [Thompson et al, JGR, 2012]
  http://croc.gsfc.nasa.gov/shadoz . Annual -> WOUDC, with links to NDACC, AVDC. In 2014 > 6K P-T-U & O3 profile sets
WHO: Anne Thompson, PI; Jacquie Witte, Archiver & International Team from host countries (Cen. & So. Am., Africa) & sponsors (Europe, US, Japan)

## Slide 6
Topic of Study | Station* | Co-I/Sponsor** | SHADOZ start year | Site start year | Network affiliation ** | Ancillary data/UACO variables | Expected sonde freq./year
Long-term Validation / Trends (Data available prior to 1995) | Kuala Lumpur | Maznorizan bt Mohamad, & YY Toh, Malaysian Met., S. Yonemura, Japan | 1998 | 1992 |  |  | 26
 | Watukosek | Ninong Komala, LAPAN & Masatomo Fujiwara, Hokkaido Univ. | 1998 | 1998 | SOWER | CFH-water vapor profiles | 26
 | Am. Samoa | Bryan Johnson & Samuel J. Oltmans, NOAA | 1998 | 1986 | NDACC / GAW | Dobson / surface CO2, CH4, CO, CFCs, O3 | 52
 | Natal | Francis J. Schmidlin, NASA/Wallops & Neusa Paes Leme, INPE | 1998 | 1979 | NDACC | Brewer | 52
 | Hilo | B. Johnson , D. Hurst & S. J. Oltmans, NOAA | 1998 | 1982 | NDACC / GAW | MLO – Dobson, FTIR, O3 Lidar, CFH-water vapor / surface CO2, CH4, CO, CFCs, O3 | 52
 | Irene | G.J.R. Coetzee, S. African Weather Serv. | 1999 | 1990 |  | Dobson | 26
 | La Reunion | Françoise Posny, Université de La Réunion | 1998 | 1998 | NDACC | SAOZ, O3 Lidar | 26
Processes in the FT, TTL, and LS | Fiji | B. Johnson & S. J. Oltmans, NOAA | 1998 | 1997 |  |  | 26
 | San Jose*** | Rennie Selkirk, NASA/GSFC & Holger Vömel, GRUAN Lead Center | 2006 | 2006 | GRUAN | SO2 sondes, CFH-water vapor profiles | 52
 | San Cristobal | B. Johnson (NOAA) & H. Voemel | 1999 | 1998 | GRUAN / SOWER | CFH-water vapor profiles | 52
 | Paramaribo | Rinus Scheele, KNMI | 1999 | 1999 | NDACC | Brewer | 52
 | Ascension Is. | Francis J. Schmidlin, NASA/Wallops | 1998 | 1990 | TCCON / GAW | Carbon columns / surface CO2, CH4, CO, CFCs | 26
 | Nairobi | Bertrand Calpini, MeteoSwiss & John Nguyo, KMD | 1999 | 1996 |  | Dobson, surface O3 | 52
 | Ha Noi | H. Gia Hiep, AMO, S. Ogino, JAMSTEC, M. Fujiwara, Hokkaido Univ., & M. Shiotani, RISH | 2005 | 2004 | SOWER | CFH-water vapor profiles | 26
* Colors for stations indicate geographic region: blue-Western Pacific, red-Atlantic/Africa, white-Subtropics, & green-Equatorial Americas
** See Acronyms in Appendix
*** Station formerly referred to as Alajuela / Heredia

## Slide 7: New “Science” from SHADOZ (1): Unique Role of Tropical Sondes
Pre-SHADOZ record at 5 sites invites trends analysis. UT/LS: 1985-> 2009, - 2-3%/decade (Randel &Thompson, 2011)
Example (1): New SHADOZ studies suggest increase in UT/LS ozone trends since 2002; imply interruption in acceleration of Brewer-Dobson circulation (Gebhardt et al., ACP, 2014; **Aschmann et al., ACPD, 2014;below)

## Slide 8: New “Science” from SHADOZ (2): Bellwether for Long-range SH Pollution
Hatched trends significant. More than 50%/decade O3 increase, 8-10 km (left) winter only, not in biomass burning season (SON)!
Back-trajectories (5-day, GSFC model) point to mixture of South American, African/Madagascar, and South Asian sources (right)
Note: these increases not observed from space!
Source: Thompson et al., ACPD, SI2N Issue, 2014
Réunion
winter

## Slide 9: SHADOZ Metrics, Impact, Archive - 1
Sondes in Archives.
* Costa Rica, Hanoi after 2005
GAPS
1999-2006:
> 400 profiles/yr
2011-2013:
< 300 profiles/yr

## Slide 10: Recent Data Gaps: Equipment Age, Personnel, Agreements, Funding
2013; Final, >300
2014? > 350

## Slide 11: SHADOZ Metrics, Impact, Archive - 2
Publications Impact (based on 130 articles)

## Slide 12: SHADOZ Archive Status, May 2014
Data gaps at 5 stations have been resolved (thanks to NOAA & partners, GSFC/WFF, INPE, SAWS)
  After 2008, gaps at Fiji, San Cristobal (Galapagos, Ecuador), Irene (So. Africa). All are operational as of 2014. Irene since 2012.
  Ascension & Natal gaps started in 2010. Natal operational, 10/13
Data Link to SHADOZ at NDACC. WOUDC data delivery from SHADOZ complete for 2012, partial for 2013.
Re-processing underway at all stations. “Homogenization” by WMO/ASOPOS Recommendation
  NOAA – Station data delivered to SHADOZ 3/14: Fiji, Samoa, Hilo. San Cristobal & Costa Rica pending.
  Underway: Nairobi, Paramaribo, Réunion, Watukosek.
  More complex: Kuala Lumpur, Hanoi, Natal & Ascension
Anticipate 2015 WMO-sonde Workshop. JOSIE?!

## Slide 13: New Technical Issues from Radiosonde Changes
  Background Current (Voemel & Diaz, 2009; Stuebi & Levrat, 2009). Implication for SHADOZ at certain sites. Addressed in “homogenization”
  New Radiosondes (RS80-> RS92->Imet). Pressure offsets! Below
  Third instrument type. SPC stable, ENSCI-> DMT change displays operational problems – impact on long-term record TBDl
  Stauffer et al., AMT, doi:10.5194/
  amt-7-65-2014.
7-8% correction 

## Slide 14: SHADOZ Status Summary
More than 6000 Ozone-PTU Profiles Sets at SHADOZ & WOUDC Archives. NDACC Link. 1998-2013
Data are key to satellite validation and trends in troposphere & lower stratosphere.
Technical reliability of ozonesonde measurement is improved by JOSIE, ASOPOS and other WMO activities
Further enhancement through 2013-2014 “Data Homogenization” effort
SHADOZ exploring affiliation with GRUAN (new radio-sonde issues)
Managers! “Mind the Gap!” (Prevent Gap)

## Slide 15: THANK YOU FOR YOUR ATTENTION! Acknowledgments & References
Support from NASA, NOAA, with JOSIE and O3-DQA sponsored by WMO.
J. Aschmann et al., Hiatus in the acceleration of tropical upwelling in the 21st century, Atmos. Chem. Phys. Disc., 2014.
C. Gebhardt, et al., Stratospheric ozone trends and variability as seen by SCIAMACHY from 2002-2011, Atmos. Chem. Phys., 14, 831-846, 2014. doi: 10.5194
H. G. J. Smit et al, Assessment of the performance of ECC-ozonesondes under quasi-flight conditions in the environmental simulation chamber: Insights from the Jülich Ozone Sonde Intercomparison Experiment, JGR, 112. D19306, doi: 10.1029/ 2006JD007308, 2007.
R. M. Stauffer et al., Propagation of radiosonde pressure sensor errors to ozonesonde measurements, Atmos. Meas. Tech., 7, 65-79. 2014. doi:10.5194/amt-7-65-2014.
  A. M. Thompson et al, Southern Hemisphere ADditional Ozonesondes (SHADOZ) 1998-2000 tropical ozone climatology. 1. Comparison with TOMS and ground-based measurements, JGR, 108, 8238, doi: 10.1029/ 2001JD000967, 2003.
  A. M. Thompson, et al., Southern Hemisphere Additional Ozonesondes (SHADOZ) 1998-2004 tropical ozone climatology. 3. Instrumentation, station variability, evaluation with simulated flight profiles, JGR, 112, D03304, doi: 10.1029/ 2005JD007042, 2007.
  A. M. Thompson et al., Strategic ozone sounding networks: Review of design and accomplishments, Atmos. Environ. 45, 2145-2163, 2011.
A. M. Thompson et al., SHADOZ (Southern Hemisphere Additional Ozonesondes) ozone climatology (2005-2009): Tropospheric and lower stratospheric profiles with comparisons to OMI-based ozone products, JGR, 117, D23301, doi: 10.1029/2011JD016911, 2012.
A. M. Thompson et al., Is tropospheric ozone over southern Africa really increasing? Evidence from sonde and aircraft profiles, Atmos. Chem. Phys. Disc., 2014.
Notes: <number>