## Slide 1
OZONE MONITORING AND RESEARCH IN POLAND
J. KRZYSCIN, B. RAJEWSKA-WIECH,
J. JAROSLAWSKI, J. BORKOWSKI, B.KOIS
Instituteof of Meteoroogy
And Water Management

## Slide 2
INSTITUTE OF GEOPHYSICS POLISH ACADEMY OF SCIENCES
BELSK OBSERVATORY
THE DOBSON MEASUREMENTS OF THE TOTAL OZONE CONTENT AND OZONE VERTICAL PROFILE BY THE UMKEHR METHOD STARTED IN 1963.
IN 1991 THE BREWER SPECTROPHOTOMETER NO.64 (SINGLE MONOCHROMATOR) WITH A UV-B MONITOR WAS INSTALLED .THE BREWER SPECTROPHOTOMETER NO. 207 (DOUBLE MONOCHROMATOR) HAS BEEN PUT INTO OPERATION IN 2010.
THE SURFACE OZONE MEASUREMENTS WITH MONITOR LABS, ML8810 METER (REPLACED BY ML9811 IN 2004) STARTED IN 1991.
SYSTEMATIC MEASUREMENTS OF GROUND LEVEL ULTRAVIOLET SOLAR RADIATION (UV-B) HAVE BEEN CARRIED OUT AT BELSK STATION SINCE MAY 1975 – UP TO NOW. (THE LONGEST UV SERIES IN EUROPE)
SPECTRAL DISTRIBUTION OF UV RADIATION HAS ALSO BEEN MONITORED WITH THE BREWER SPECTROPHOTOMETERS AT BELSK SINCE 1992 (BREWER NO.64) AND SINCE 2010 (BREWER NO.207).

## Slide 3: INSTITUTE OF METEOROLOGY AND WATER MANAGEMENT
THE OZONE SOUNDINGS HAVE BEEN PERFORMED AT LEGIONOWO (52.40N, 20.97E) UPPER-AIR STATION SINCE 1979. NOW THE ECC OZONE SENSOR AND DIGICORA/RS80/92 RADIO SOUNDING SYSTEM OF VAISALA ARE IN USE.
SURFACE OZONE MEASUREMENTS WITH MONITOR LABS. ML9810 ARE PERFORMED AT 3 STATIONS.
BROADBAND UV BIOMETERS MODEL SL 501 VERS. 3 HAVE BEEN USED FOR UV MEASUREMENTS AT THREE IMWM STATIONS. SINCE 2006, BROADBAND OPTIX UVEM-6C HAVE BEEN USED FOR NOWCASTING PURPOSES AT SIX IMWM STATIONS.
TWO NILU-UV SPECTRAL FILTER INSTRUMENTS INSTALLED AT IMMW STATION LEGIONOWO MEASURE THE UV-B, UV-A, TOTAL OZONE AND CLOUD TRANSMISSION.

## Slide 4: INFORMATION TO THE PUBLIC
SINCE 2000, THE UV INDEX FORECAST FOR POLAND HAS BEEN AVAILABLE FROM MAY TO SEPTEMBER ON IMWM WEB PAGES.
SINCE 2006, AN OPERATIONAL MONITORING OF UV INDEX FROM THE IMWM NETWORK HAS BEEN PUBLISHED ON IMWM WEB PAGES.
AN INFORMATION SYSTEM OF SOLAR UV RADIATION FOR OUTDOOR WORKERS WAS DEVELOPED IN THE FRAME OF PROJECT ‘DETERMINATION OF UV RADIATION ON POLISH TERRITORY FOR THE PURPOSES OF RISK ASSESSMENT’. (IMWM)
SINCE 2001, THE DAILY MEANS OF TOTAL OZONE FROM THE DOBSON MEASUREMENTS AT BELSK AND UV INDEX FROM THE SL501A MEASUREMENTS ARE DISPLAYED IN ALMOST REAL TIME ON WEB PAGES HTTP://OZON.IGF.EDU.PL AND HTTP://UVB.IGF.EDU.PL, RESPECTIVELY. (IGF PAS)

## Slide 5
„….LONG-TERM MEASUREMENTS REPRESENT AN EXTREMELY IMPORTANT RESOURCE, AND THE CONTINUED AND INCREASED EXPLOITATION OF THESE DATA FOR SCIENTIFIC PROCESS STUDIES IS STRONGLY RECOMMENDED.”
(REPORT OF THE EIGHTH MEETING OF THE OZONE RESEARCH MANAGERS 2011)

## Slide 6
TOTAL OZONE MONTHLY MEANS FROM THE DOBSON SPECTROPHOTOMETER MEASUREMENTS AT BELSK IN THE PERIOD MARCH 1963-DECEMBER 2012.
Krzyścin, J.W., Rajewska-Wiech, B., Jarosławski, J., (2013) The long-term variability of atmospheric ozone from the 50-yr observations carried out at Belsk Tellus B 2013, 65, 21779, http://dx.doi.org/10.3402/tellusb.v65i0

## Slide 7
THE LONG TERM MONTHLY MEANS OF OZONE CONTENT FOR 1962-1967 AND 1988-2012 PERIOD AND RELATIVE DIFFEENCES BETWEEN MEANS
Krzyścin, J.W., Rajewska-Wiech, B., Jarosławski, J., (2013) The long-term variability of atmospheric ozone from the 50-yr observations carried out at Belsk Tellus B 2013, 65, 21779, http://dx.doi.org/10.3402/tellusb.v65i0

## Slide 8: FRACTIONAL DEVIATIONS OF THE TOTAL OZON MONTHLY MEANS FROM LONG TERM (1963-2012) IN PERCENT OF LONG TERM MEAN
Krzyścin, J.W., Rajewska-Wiech, B., Jarosławski, J., (2013) The long-term variability of atmospheric ozone from the 50-yr observations carried out at Belsk Tellus B 2013, 65, 21779, http://dx.doi.org/10.3402/tellusb.v65i0

## Slide 9: RESEARCH SUBJECTS
DEVELOPING A NOVEL TREND MODEL TO DISCLOSE THE TEMPORAL VARIABILITY OF THE LONG-TERM COMPONENT OF THE OZONE VARIABILITY THE MODEL HAS BEEN USED FOR THE TREND DETECTION IN THE GLOBAL SATELLITE AND BELSK’S OZONE DATA.
CALCULATION OF THE VERTICAL PROFILE OF OZONE FROM THE UMKEHR OBSERVATIONS USING NEURAL NETWORK APPROACH.
DEVELOPING A MULTIPLE REGRESSION MODEL TO ATTRIBUTE THE ARCTIC TOTAL OZONE VARIABILITY TO VARIOUS CHEMICAL AND DYNAMICAL OZONE FORCING FACTORS.
MODELLING BIOMEDICAL ASPECTS OF SOLAR AND ARTIFICIAL UV RADIATION. DEVELOPING SCENARIOS FOR GETTING THE APPROPRIATE VITAMIN D LEVEL DUE TO SOLAR RADIATIONS AND BASIS FOR ANTI-PSORIASIS HELIOTHERAPY IN POLAND HAVE BEEN PREPARED
FINDING THE IMPACT OF EYJAFJALLAJOKULL VOLCANO ASH ON SURFACE UV AT BELSK.