## Slide 1
Ozone and UV Radiation Observational Activities in Turkey
Serpil YAĞAN
Climatology Division
Research Department
Turkish State Meteorological Service
WMO/UNEP 9 th Ozone Research Managers Meeting
14-16 May 2014, Geneva

## Slide 2
THE PROTECTION OF THE OZONE LAYER STUDIES IN TURKEY
Responsible for measurements of ozone and ultraviolet radiation
The protection of ozone layer studies carried out under the coordination of MoE&U.
Vienna Convention and Montreal Protocol regulation national contact point.

## Slide 3
Main Building of Turkish State Meteorological Service
The Turkish State Meteorological Service, TSMS, was founded in 1937. It is the only legal organization which provides all meteorological information in Turkey.
Brewer188 Place

## Slide 4
Turkish State Meteorological Service (TSMS) is responsible for observing and promoting research activities on measurements of ozone and UV radiation.
OBSERVATIONAL ACTIVITIES
  Ozone measurements
    Brewer Spectrophotometer MKIII#188 (Column)
    Ozonesonde-ECC (Profile)
  UV measurements
    Broad band (Model 501 UV-Biometer)
    Narrow band (UVR1-B Radiometer)

## Slide 5
Ozone Measurement (Brewer) only Ankara
UV Measurement
Ankara, Akçaabat, Aksaray, Elazığ, Göksun, Mardin, Oltu, Sivas, Tarsus, Tokat, Van, İstanbul, İzmir, Antalya-Kale, Afyon-Çay (15 stations)
ANKARA (Capital City) (39°58 ’N; 32°52 ’E) 912 m

## Slide 6
Brewer Spectrophotometer MKIII#188
  Daily automatic measurements of total ozone since November 2006,
  Ankara station which is the component of World Meteorological Organization (WMO) - Global Atmosphere Watch Programme (GAW),
  Data is stored in the database of Research and Data Processing Section of TSMS,
  Also sent to the World Ozone and UV Radiation Data Center (WOUDC) in Toronto, Canada.
OZONE MEASUREMENT

## Slide 7
Ankara (Station ID 348).

## Slide 8
Maximum Brewer ozone value is 479 DU (18 March 2010) and the minimum ozone value is 245 DU (10 November 2009), the mean value is 319 DU (2006-2013) of Ankara.

## Slide 9
Monthly mean values of total column ozone in Ankara (2007 - 2013).
The mean of the spring ozone is 354 DU, the mean of the autumn ozone is 287 DU between 2007 and 2013 period.
The seasonal variability of ozone in Ankara, Turkey is characterized by a maximum in spring and a minimum in autumn.
As you see, both graphics are compatible with each other.

## Slide 10
Ozonesonde-ECC (Profile)
Ozone measurements with ozonesonde were started by the TSMS at 13 th of January 1994 in Ankara.
Total 398 balloon have been launched and 366 daily total ozone column data have been obtained from 1994 to April 2013.
The 32 observations could not be performed due to the different reasons such as early exploding of the balloon or weak signals from the instrument.

## Slide 11
Maximum ozone partial pressure is at approximately 22-24 km and minimum temperature is at 16-18 km in Ankara.

## Slide 12
Maximum ozone values are in winter and spring seasons at 22-24 km,
Summer season maximum ozone is at 24-26 km,
Autumn season maximum ozone is at 24-26 km,
Long term mean maximum ozone is at 22-24 km.

## Slide 13
UV MEASUREMENTS
UV radiometers are used to measure UV radiation at 14 stations in narrow band and at 1 station in broad band with varied instruments.
Broad band measurements:
UV-Biometer Model 501 is used for broad band UV radiation measurements.
Narrow band filter instrument:
UVR1-B Global Spectral Radiometers are used for narrow band UV radiation measurements.
Spectroradiometers:
Brewer spectrophotometer MKIII #188 is used for spectral UVB measurements in Ankara station.

## Slide 14
CALIBRATION ACTIVITIES
Calibration of Brewer spectrophotometer #188 MK III has been performed biennially.
First Brewer S. calibration was carried out by International Ozone Services Inc. (IOS-Mr.Ken Lamb) which provides worldwide ozone and UV calibration services to customers with Brewer Ozone Spectrophotometer instruments.
Calibration activities were financially supported by the WMO.
IOS used Brewer Ozone Spectrophotometer #017 as a reference instrument on 07–12 October 2008 in Ankara station.

## Slide 15
Second Brewer S. calibration was carried out by Kipp& Zonen (Mr. Arjan Hoogendoorn) on 22–29 September 2010.
Kipp& Zonen used Brewer Ozone Spectrophotometer #158 as a reference instrument in Ankara station.

## Slide 16
Third calibration of Brewer S. #188 was carried out from 23 to 27 September in 2013 by Kipp& Zonen (David Godoy Alonso).
Kipp& Zonen used Brewer Ozone Spectrophotometer #158 as a reference instrument in Ankara station.

## Slide 17
RESULTS FROM OBSERVATIONS AND ANALYSIS
Comparison of TOMS (OMI) from satellite with the total ozone measurements of Brewer#188;
The DS ozone data period used in this analysis ranges from November 2006 to December 2013 Brewer#188 and the same period for the TOMS (OMI) ozone data.
The obtained results (correlation coefficient is R=0.97) indicates that the used equipments operating satisfactorily.

## Slide 18
Data reporting
Products of ozone and UV radiation measurements are stored at the Research and Data Processing Section of TSMS and can be accessible through internet to users.
DISSEMINATION OF RESULTS

## Slide 19
All data measured by Brewer Spectrophotometer MK III #188 are sent regularly to the World Ozone and UV Radiation Data Center (WOUDC). They are archieved and published with the station number 348 in Toronto, Canada.

## Slide 20
Information to the public
A TUBITAK project, titled “Observing the Variability in the Troposferic and Stratosferic Ozone and UVB measurements and Analyzing the Results”, was conducted at TSMS under the collaboration with some scientist from Istanbul Technical University and completed in 2008.
As a result, a statistical model was developed to forecast daily total ozone and UV index.
The model runs for 125 stations in Turkey and 5 stations in the Turkish Republic of Northern Cyprus and the model results are published through internet web site.
http://www.mgm.gov.tr/kurumici/tahmin-ozon-mgm.aspx

## Slide 21
TSMS Model output for ozone and UV index forecast in TURKEY.

## Slide 22
MGM and the German Meteorological Service (DWD) have been cooperation for ozone and ultraviolet index forecast. Daily total ozone and ultraviolet index forecast information, which is produced by DWD for Turkey’s 125 points and Northern Cyprus Turkish Republic (TRNC)’s 5 points, are published through internet web site. http://www.mgm.gov.tr/kurumici/tahmin-ozon-mgm.aspx

## Slide 23
RESULTS
Data set for ozone profile has been created by the TSMS since 1994.Ozonsonde observations have been finished in March 2013.
TSMS became a member of the WOUDC in 1998 and take place in global ozon observing network.
TSMS developed ozone and UV index forecasting model as a result of a TUBITAK Project completed in 2008.
It has been included in national monitoring system Brewer Spectrophotometer such a new technology.
Systematic observations began for monitoring long term changes in ozone and UV radiation.

## Slide 24
RESULTS
Daily publishing the model output for Ozone and UV index forecasts, the TSMS has taken an important step in informing public.
Regular UV radiation measurements began firstly in Ankara and Antalya in 1997. Today, UV radiation is measured in 15 different stations.
A data set for UV radiation has been created by using these measurements.

## Slide 25
THANKS
syagan@mgm.gov.tr
yagans@gmail.com